## Slide 1
The Use of On-Demand Forecasts for Weather Optimization of Aircraft Tracks
Ólafur Rögnvaldsson – IMR/UiB
Einar I. Andrésson – RU
Þorgeir Pálsson – RU

## Slide 2
Numerical Weather Models
  Importance of resolution
Routing optimization using NWM
Current Crisis Response System
  SARWeather general description
Use of observations from UAS’s
On-going research
Conclusions
Overview
SARWeather

## Slide 3
Importance of high resolution
Global forecasts
15-50 km grid
SARWeather forecasts
9 – 3 – 1 km grids
SARWeather

## Slide 4
Importance of high resolution
When model resolution is increased to 1 km the true complexity and strength of the wind field becomes apparent
Very high resolution – 1 km
Medium resolution – 9 km
SARWeather
Atmos. and Meteorological Instrumentation – EGU 2012

## Slide 5
Why not always use 1km resolution?
Chart: Grid size [km]
Need 1000-times more CPU power to simulate a 1 km resolution forecast than a 10 km one for the same region!
SARWeather
Atmos. and Meteorological Instrumentation – EGU 2012

## Slide 6
You only need high very high resolution once in a while?
Computer clouds (e.g. Azure, EC2 and GreenQloud) are starting to offer HPC service
Offers great scalability
Relatively cheap
And there is already a solution out there 
What if
SARWeather

## Slide 7
Recent M.Sc. project at the RU aimed at minimize fuel burn and emissions by optimizing flight tracks with respect to wind
Used the Dijkstra search algorithm
Used data from Icelandair
  Keflavík – New York flight @ 2011-07-14
  Keflavík – Copenhagen flight @ 2011-07-14
  Boeing 757-200
Fuel savings estimated using the BADA model
Routing optimization

## Slide 8
Reykjavík ATC area
Reykjavík Air Traffic Control area (BIRD)
Over 110.000 flights in 2011
Average time spend within BIRD was 100 minutes
1% fuel savings would amount to 6.000 metric tons
SARWeather

## Slide 9
NWM area
Weather was simulated over a large region @ 9km resolution
Part of domain used to optimize the routes between Keflavík and New York and Keflavík and Copenhagen

## Slide 10
Flight ICE615 – Keflavík New York
SARWeather

## Slide 11
Flight ICE204 – Keflavík/Copenhagen
SARWeather
Similar results found for another flight @ 2011-07-14
Approximately 1% fuel savings for the whole flight
Note that there was not “much” weather during this day
Perhaps more to be gained in stronger winds?

## Slide 12
Good weather information help improve decision making
Current CRS uses the WRF model and consists of a
  Backend and Frontend
Frontend is called SARWeather
  Easy to use
  Fast
  Flexible model output and presentation
    CF and ArcGIS compliant output files
    Interactive and static maps
Crisis Response System
SARWeather

## Slide 13
SARWeather
Choose resolution:
1, 3, or 9 km
SARWeather
Give the forecast a name
Type in Lat/Lon or click on the map

## Slide 14
SARWeather
Choose domain size
SARWeather
Give the forecast a name
Type in Lat/Lon or click on the map

## Slide 15
SARWeather
Atmos. and Meteorological Instrumentation – EGU 2012
Choose forecast duration
SARWeather
Give the forecast a name
Type in Lat/Lon or click on the map

## Slide 16
SARWeather
1km resolution, 84x84 km domain and 24 hr forecast
Do you need CF or ArcGIS compliant output files?
When all is set, run forecast
SARWeather
Give the forecast a name
Type in Lat/Lon or click on the map

## Slide 17
SARWeather
Time slider
Chose variable
Control transparency
Zoom
Time from initiation:
30 sec – computer node up’n running
2 min 40 sec – pre-processing done and model starts running
5 min 50 sec – first frame ready on screen
51 min 50 sec – 24 hr forecast ready
54 min 20 sec – “static” post-processing done
Typical response time for SAR operators is 30 min or less
SARWeather

## Slide 18
Simulated and observed surface winds
on 15 July 2009 at 13 UTC
WRF at a resolution of 500 m forced with ECMWF-data on model levels.
Observed surface winds in red
Mt. Esja
High resolution not always sufficient
Model simulates a see-breeze that is not seen in observations
SARWeather

## Slide 19
SUMO and WRF
The SUMO (Small Unmanned Meteorological Observer) can measure winds, humidity, pressure, and temperature in a vertical profile up to a 4km height
SARWeather

## Slide 20
SUMO and WRF
This data can be assimilated with the WRF weather forecast
SARWeather

## Slide 21
The SUMO-data is incorporated into the WRF-simulation, via obs-nudging
SUMO and WRF
SARWeather

## Slide 22
Simulated and observed surface winds
on 15 July 2009 at 13 UTC
WRF at a resolution of 500 m forced with ECMWF-data on model levels and SUMO data
Observed surface winds in red
Mt. Esja
Effects of additional observations
The flow structure is now in much better agreement with available observations
SARWeather

## Slide 23
Simulated flow in N-S section across Mt. Esja
No extra observations
Wrong!
A major difference in flow pattern extending far above mountain top leve
23 km
Wind speed, ranging from 0 to 12 m/s
Effects not just at the surface
SARWeather

## Slide 24
Effects can be far reaching
CTRL - ObsNudge
Marius O. Jonassen, Haraldur Ólafsson,
Hálfdán Ágústsson, Ólafur Rögnvaldsson, and Joachim Reuder (2012). Improving a high resolution numerical weather simulation by assimilating data from an unmanned aerial system. Accepted for publication in Monthly Weather Review
“Substantial improvements of winds, temperatures and humidity in the region are achieved”
50 km
SARWeather

## Slide 25
The SUMO has been equipped with an optical dust sensor
Additional sensors
GP2Y1010AU0F is a dust sensor by optical sensing system:
An infrared emitting diode (IRED) and an phototransistor are diagonally arranged into the device
It detects the reflected light of dust in air
Especially effective to detect very fine particle
In addition it can distinguish smoke from house dust by pulse pattern of output voltage
Saturation at about 500μg/m3
SARWeather

## Slide 26
The SUMO dust sensor has been tested in France and Iceland
Preliminary results
SARWeather

## Slide 27
The SUMO dust sensor has been tested in France and Iceland
Preliminary results
Sensor is now being calibrated and tested
with ash from Mt. Eyjafjallajökull
Ascending
Descending
SARWeather

## Slide 28
Calibration – preliminary results
SARWeather
The sensor (BU) readings show high sensitivity in the range 125 – 300. After that the sensitivity is rather low in the range 350 to 700.
Using the meter for ash surveillance for jet aircrafts, the best thing would be to designate below 300 as “safe” but above 400 as “unsafe”

## Slide 29
Various uses of model output
To correctly simulate distribution of pollutants, it is very important to correctly simulate the atmospheric conditions close to the source.
Data courtesy of Prof. Saji Hameed at the University of Aizu, Fukushima.
SARWeather

## Slide 30
System schematics
Data assimilation
(optional)
Data source for atmospheric model
Misc. datasources (optional)
User interface
Current research and development
Integration with other systems
D4H
GDACS
MapAction
SARWeather

## Slide 31
System schematics
SARWeather
Optional module
Still under development
Integration with other systems
D4H
GDACS
MapAction
User interface
Data assimilation
(optional)
Misc. datasources (optional)
Data source for atmospheric model
Current research and development

## Slide 32
Model resolution is important
  Especially in the vicinity of complex terrain
Additional observations can improve the simulation
  Vertical profiles made by the SUMO
The SUMO is a low-cost system with many advantages
  Proof of concept before investing in a more durable and expensive UAS
  Additional sensors are being added to the system
Fast response time is crucial in SAR operations
  SARWeather meets these needs
  Good weather information help improve decisions
The SUMO is currently being integrated to the SARWeather, on-demand, Crisis Response System
Conclusions
SARWeather

## Slide 33: Acknowledgement
SARWeather is a joint research project led by IMR/Belgingur, in collaboration with NOAA/ESRL, the University of Bergen, and the private companies GreenQloud and DataMarket. To ensure maximum usability for SAR operators, SARWeather is developed in close collaboration with ICE-SAR and the Civil Protection Department of the Icelandic Police.
SARWeather was initially funded in part by grant number 550-025 (Vejrtjeneste for Søberedskab) from NORA and by the European Commission under the 7th Community Framework Programme for Research and Technological Development (GalileoCast). GalileoCast is managed by GSA, the European GNSS Supervisory Authority.
Current development of SARWeather is funded in part by the Icelandic Technical Development Fund – RANNÍS
Development related to the SUMO has in part been funded by the COST project ES0802
SARWeather
Atmos. and Meteorological Instrumentation – EGU 2012