## Slide 1
Small unmanned airplanes
In-situ observations of airborne dust/ash and improved local weather forecasts
Ólafur Rögnvaldsson – IMR/UiB
Hálfdán Ágústsson – IMR/UI/IMO
Haraldur Ólafsson – UI/UiB/IMO
Marius O. Jonassen – UiB/IMR
Measurements and simulations of volcanic ash for civil aviation

## Slide 2
Atmospheric models
  Global vs. regional
  The WRF model
Importance of resolution
Use of observations from UAS’s
  The SUMO system
On-going research
  SARWeather and SUMO
Conclusions
Overview
Measurements and simulations of volcanic ash for civil aviation

## Slide 3
Atmospheric models
Measurements and simulations of volcanic ash for civil aviation
Set of equations that describe the atmospheric flow and need to be integrated forward in time to produce a weather forecast

## Slide 4
Open source model developed in collaboration of
  NCAR, NOAA, FSL, AFWA, NRL, Univ. of Oklahoma & FAA
Five development teams with sixteen workgroups
  More than 160 official developer
  Additional development by academic and governmental institutions in the US and abroad
  Very large user community, excellent support
Non-hydrostatic
Regional and global applications
Wide range of scales for both real time and idealized applications
  Optional data assimilation (3D-VAR, 4D-VAR, and FDDA)
  Has been modified for volcanic applications
  Includes a dust module (re-suspension of dust/ash)
The WRF atmospheric model
Measurements and simulations of volcanic ash for civil aviation

## Slide 5
Importance of high resolution
Global forecasts
15-50 km grid
SARWeather forecasts
9 – 3 – 1 km grids
Measurements and simulations of volcanic ash for civil aviation

## Slide 6
Importance of high resolution
How does the weather model “see” this mountain?
Measurements and simulations of volcanic ash for civil aviation

## Slide 7
Importance of high resolution
Vatnajökull icecap, max height is 1675m. Top height of Mt. Öræfajökull is only 880m
At 1km resolution the max height is 2020m. Top height of Mt. Öræfajökull is now 1945m
Measurements and simulations of volcanic ash for civil aviation

## Slide 8
Importance of high resolution
Measurements and simulations of volcanic ash for civil aviation
9 km resolution

## Slide 9
Importance of high resolution
Measurements and simulations of volcanic ash for civil aviation
3 km resolution

## Slide 10
Importance of high resolution
Measurements and simulations of volcanic ash for civil aviation
1 km resolution

## Slide 11
Simulation results are also affected by the choice of parameterization schemes
Rögnvaldsson, Ó., Bao, J.-W., Ágústsson, H., and Ólafsson, H.: Downslope windstorm in Iceland – WRF/MM5 model comparison, Atmos. Chem. Phys., 11, 103-120, doi:10.5194/acp-11-103-2011, 2011.
Measurements and simulations of volcanic ash for civil aviation

## Slide 12
Why not always use 1km resolution?
Chart: Grid size [km]
Need 1000-times more CPU power to simulate a 1 km resolution forecast than a 10 km one for the same region!
Measurements and simulations of volcanic ash for civil aviation

## Slide 13
Simulated and observed surface winds
on 15 July 2009 at 13 UTC
WRF at a resolution of 500 m forced with ECMWF-data on model levels.
Observed surface winds in red
Mt. Esja
High resolution not always sufficient
Measurements and simulations of volcanic ash for civil aviation
Model simulates a see-breeze that is not seen in observations

## Slide 14
SUMO and WRF
The SUMO (Small Unmanned Meteorological Observer) can measure winds, humidity, pressure, and temperature in a vertical profile up 4km height
Measurements and simulations of volcanic ash for civil aviation

## Slide 15
SUMO and WRF
This data can be assimilated with the WRF weather forecast
Measurements and simulations of volcanic ash for civil aviation

## Slide 16
The SUMO-data is incorporated into the WRF-simulation, via obs-nudging
Measurements and simulations of volcanic ash for civil aviation
SUMO and WRF

## Slide 17
Simulated and observed surface winds
on 15 July 2009 at 13 UTC
WRF at a resolution of 500 m forced with ECMWF-data on model levels and SUMO data
Observed surface winds in red
Mt. Esja
Effects of additional observations
Measurements and simulations of volcanic ash for civil aviation
The flow structure is now in much better agreement with available observations

## Slide 18
Simulated flow in N-S section across Mt. Esja
No extra observations
Wrong!
A major difference in flow pattern extending far above mountain top leve
23 km
Wind speed, ranging from 0 to 12 m/s
Effects not just at the surface
Measurements and simulations of volcanic ash for civil aviation

## Slide 19
Effects can be far reaching
Measurements and simulations of volcanic ash for civil aviation
CTRL - ObsNudge
Marius O. Jonassen, Haraldur Ólafsson,
Hálfdán Ágústsson, Ólafur Rögnvaldsson, and Joachim Reuder (2012). Improving a high resolution numerical weather simulation by assimilating data from an unmanned aerial system.
Monthly Weather Review, in revision
“Substantial improvements of winds, temperatures and humidity in the region are achieved”
50 km

## Slide 20
The SUMO has been equipped with an optical dust sensor
Additional sensors
Measurements and simulations of volcanic ash for civil aviation
GP2Y1010AU0F is a dust sensor by optical sensing system:
An infrared emitting diode (IRED) and an phototransistor are diagonally arranged into the device
It detects the reflected light of dust in air
Especially effective to detect very fine particle
In addition it can distinguish smoke from house dust by pulse pattern of output voltage
Saturation at about 500μg/m3

## Slide 21
The SUMO dust sensor has been tested in France and Iceland
Preliminary results
Measurements and simulations of volcanic ash for civil aviation

## Slide 22
The SUMO dust sensor has been tested in France and Iceland
Preliminary results
Measurements and simulations of volcanic ash for civil aviation
Sensor is now being calibrated and tested
with ash from Mt. Eyjafjallajökull
Ascending
Descending

## Slide 23
Various uses of model output
To correctly simulate distribution of pollutants, it is very important to correctly simulate the atmospheric conditions close to the source.
Data courtesy of Prof. Saji Hameed at the University of Aizu, Fukushima.
Measurements and simulations of volcanic ash for civil aviation

## Slide 24
System schematics
Data assimilation
(optional)
Data source for atmospheric model
Misc. datasources (optional)
User interface
Current research and development
Measurements and simulations of volcanic ash for civil aviation
Integration with other systems
D4H
GDACS
MapAction

## Slide 25
System schematics
SARWeather
Optional module
Still under development
Integration with other systems
D4H
GDACS
MapAction
User interface
Data assimilation
(optional)
Misc. datasources (optional)
Data source for atmospheric model
Current research and development
Measurements and simulations of volcanic ash for civil aviation

## Slide 26
The WRF model has a wide variety of applications
Model resolution is important
  Especially in the vicinity of complex terrain
Additional observations can improve the simulation
  Vertical profiles made by the SUMO
The SUMO is a low-cost system with many advantages
  Proof of concept before investing in a more durable and expensive UAS
  Additional sensors are being added to the system
  Dust sensor could detect low concentrations of ash above airports (fly vs. no fly)
The SUMO is currently being integrated to the SARWeather, on-demand, forecasting system
Conclusions
Measurements and simulations of volcanic ash for civil aviation